## Slide 1: Vaccine Management in Schools
August 2023
Carol Henry
Specialist Pharmacy Technician
Pharmacy Distribution Centre

## Slide 2: Learning Outcomes
Use of vaccine porter in schools.
How to receive an order of vaccine within school setting.
How to maintain cold chain using porter and cool packs.

## Slide 3: Whose Responsibility is it?
The overall responsibility for the storage of vaccine remains with the Registered Healthcare Practitioner or Healthcare Support Worker administering the vaccine.
They must ensure the vaccines have been stored in accordance with the manufacturer's recommendations BEFORE they are administered.

## Slide 4: Validated porter and conditioned cool packs
Porter and cool packs used to maintain the cold chain at +2 C to + 8 C, used for transportation and storage of vaccine during clinic/school setting.
Only validated for a maximum number of hours with a minimum number of openings.
+2 C to + 8 C ensures the efficacy of the vaccine and maintains their effectiveness.
Use “USE FIRST” stock as a priority.

## Slide 5: Vaccine porter helapet 24
The vaccine porter 24 maintains temperatures within the system between 2 ͦC and 8 ̊C for 8 hours. Eight Medicool packs are used in the validation design and multiple openings are incorporated into the 8 hour validated period within a clinic setting.
** 9 hour validation for schools.
Each vaccine porter will have a data logger placed on top of the bottom 2 cool packs (DO NOT TOUCH OR REMOVE).
Ensure cool packs and lid are replaced ASAP and minimize number of openings to ensure validation period.
Keep porter away from heat source (radiators/underfloor heating).
Porter and vaccine “FRAGILE” – handle with care.
Notes: <number>

## Slide 6: Vaccine porter helapet 24
Each vaccine porter will be numbered and labelled with contents on the outside.
Notes: <number>

## Slide 7: Data logger graph

## Slide 8: Data logger and report

## Slide 9: Delivery check list
Expected delivery time is approx. 8-8.30am
Expected delivery time for 2nd drop (where applicable) approx. 11.30am
Pick up time approx. 3pm (primary) and 3.45pm (high school).
Ensure school staff/janitor know where vaccine has to be uplifted from (gym hall/office etc). MUST be left in a secure room.
If expecting to finish early, contact transport office 0141-211-6560 for early uplift, if possible.
Sharp boxes and tissues will be supplied with vaccine.

## Slide 10: Returned stock to PDC
Any vaccine that has been removed from the vaccine porter, no matter for how short a time, cannot be returned to the pharmacy and must be discarded. DO NOT RETURN TO PORTER.
Return stock in same porter delivered in.
ALL data will be downloaded and reviewed.
ALL returned stock will be risk assessed at PDC.
Ensure stock fit for re-issue.
Notes: <number>

## Slide 11: Vaccine stock
Vaccine check - It is the responsibility of nursing staff to record correct vaccine and batch number.
Vaccine returns – Return stock in same porter and bag issued in.
Do not remove vaccine packs from porter if they are not going to be utilised even if unopened, once the pack is taken out of the porter it cannot be returned for re-use.

## Slide 12: Fluenz stock
Product license allows vaccine to be transported and stored at ambient temperature for up to 12 hours maximum, and must be destroyed thereafter.
% (TBC) of stock supplied ambient and cold chain
Use AMBIENT stock 1st –
Return stock in same container issued (porter)
Do not return split packs or ambient stock.
Notes: <number>

## Slide 13: Minimise waste
Limit openings as much as possible. Remove the minimal amount of vaccine for use at any one time (e.g. only enough for the next hours’ worth of scheduled appointments a time)
No longer re-issuing split boxes.
End of session – share open box of vaccine.

## Slide 14: Contacts
Vaccine supply - Pharmacy Distribution Centre 0141-201-3488 or email vaccines@ggc.scot.nhs.uk
Pharmacy Public Health – 0141-201-4424
Transport Office – 0141-211-6560