## Slide 1: Vaccine Management in Schools
Karen Pawelczyk

## Slide 2: Learning Outcomes
Maintaining the cold chain
Use of vaccine porter in schools to maintain cold chain
What to look out for when you receive delivery
Stock rotation to reduce waste

## Slide 3: “Cold Chain”

## Slide 4
The cold chain is the system of transporting and storing vaccines within the safe temperature range of
+2 C to + 8 C.
It begins with the manufacturer and ends with the provider at the time of administration
The efficacy of vaccines depends on maintaining the cold chain.

## Slide 5: Journey

## Slide 6: Whose Responsibility is it? • The overall responsibility for the storage of vaccine remains with the Registered Healthcare Practitioner or Healthcare Support Worker administering the vaccine. • They must ensure the vaccines have been stored in accordance with the manufacturer's recommendations BEFORE they are administered.

## Slide 7
The vaccine porter 24 maintains temperatures within the system between 2 ͦC and 8 ̊C for 8 hours. Eight Medicool MC3 packs are used in the validation design and multiple openings are incorporated into the 8 hour validated period. The picture on the right shows a vaccine porter 24 ready to send and the picture on the left shows the inside of a porter box with two cool packs top and bottom and one cool pack on each of the four sides.

## Slide 8: Checklist for delivery
Delivery 8am -8.30am
Pick up 3.15pm -3.45pm
Stock check, replace lid and medicools as advised ASAP

## Slide 9: Guidance for storing porter at school
Porter must be stored away from radiator
Fragile polystyrene handle carefully
Limit openings as much as possible
Ensure medicools packed correctly and lid replaced firmly

## Slide 10: Validation

## Slide 11
Vaccine porter will be clearly labelled indicating priority issue vaccine enclosed. Staff must use this stock before opening vaccine porter with new supplies
PDC risk assess all vaccine returns and review data to ensure suitable for re-issue.
DO NOT TOUCH OR REMOVE LOG TAG FROM HELAPET.
MINIMISE THE NUMBER OF OPENINGS TO ENSURE COLD CHAIN IS MAINTAINED

## Slide 12: Vaccine check It is the responsibility of nursing staff to record correct batch number Vaccine Returns When returning vaccines staff must ensure they return stock in same bag they received their stock .

## Slide 13: Fluenz Tetra
Product licence allows vaccine to be transported out with cold chain for 12 hours but must be destroyed thereafter
% ambient
% cold chain
Unused returns – return in container received

## Slide 15: Minimise waste
No longer recycling open packs
Ensure vaccine porter marked priority use is first
Cin bins and tissues will be supplied with Flu vaccine only. Secondary school campaigns vaccine only will be supplied

## Slide 16: Vaccine storage and delivery managed by PDC 0141-201-3488 Pharmacy Public health 0141- 201-4424